## Slide 1: Construction Safety A summary of various hazards and their remedies in light of OSHA (Part 2)
Faizan Shafique

## Slide 2: Stairs and Ladders

## Slide 3: Difference

## Slide 4: Hazards
Stairways and ladders cause many injuries and fatalities among construction workers
About half the injuries are caused by slips, trips and falls from ladders and stairways

## Slide 5: Requirement
There must be a stairway or ladder at points of access where there is an elevation break of 0.5m (19 inch) or more.
0.5m
Break in elevation

## Slide 6: Stairs
Install between 30 and 50 degrees.
Must have uniform riser height and tread depth, with less than a 1/4-inch variation.
Uniform - 30 & 50 deg. angle
No more than 1/4 inch
variation in any stairway system
Uniform - 30 & 50 deg. angle
No more than 1/4 inch
variation in any stairway system

## Slide 7: Stairs
As a rule of thumb, The riser must not be more than 8” and tread not less than 11”

## Slide 8: Stair rails
Stairways with four or more risers or more than 30 inches high must have a stairrail along each unprotected side or edge.

## Slide 9: Stair-rail requirements
Rails must be able to withstand a force of about 100 Kgs
The height of stair-rails must be 36 inches, measured from the nose of the stairs to the top of the rail.

## Slide 10: Ladder angle
Non-self-supporting ladders:
(which lean against a wall or other support)
  Position at an angle where the horizontal distance from the top support to the foot of the ladder is 1/4 the working length of the ladder

## Slide 11: Ladder Rail Extension
When using a portable ladder for access to an upper landing surface, the side rails must extend at least 3 feet above the upper landing surface

## Slide 12: Cranes

## Slide 13: Cranes
Cranes is a broad class of construction equipments used for lifting and placing loads. A crane uses one or more machines like a hoist to produce mechanical advantage and thus move loads beyond the normal capability of a human. They can be used both to lift and lower materials and to move them horizontally.

## Slide 14: Excavations
HOIST
JIB
BOOM
Counter Weight
Hoist - Used to lift and lower load.
Boom – An inclined spar, strut, or other long member supporting the hoist
Jib – Extension attached to the boom point to provide added boom length for lifting specified loads.

## Slide 15: Major causes of crane accidents
Contact with power lines
Overturns and Falls
Mechanical failures

## Slide 16: Crane hazards
Improper loading
Excessive speeds
No hand signals
Inadequate inspection and maintenance
Unguarded swing radius
Working too close to power lines
Shattered windows
No steps/guardrails walkways
No boom angle indicator

## Slide 17: Crane hazards

## Slide 18: Thank you for listening